## Slide 1: Design and Configure a Small Company Network Using VLANs Company Network Design

## Slide 2: BY THE FOLLOWING: NUELLA EMMANUELA SUCCESS SILAS

## Slide 3: Introduction
A company network was divided using VLANs to improve security and organization.
Each department has its own VLAN and IP network.

## Slide 4: Project Scenario
Departments:
• Admin
• IT
• HR
• Sales
• Reception
Requirements:
• Separate VLANs
• Different IP networks

## Slide 5: Objectives
1. Design network topology
2. Configure VLANs
3. Assign IPs
4. Configure switches
5. Test connectivity

## Slide 6: Network Topology

## Slide 7: VLAN Table
Admin–10
IT–20
HR–30
Sales–40
Reception–50

## Slide 8: IP Addressing
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
192.168.4.0/24
192.168.5.0/24

## Slide 9: Switch Configuration
Enable
Configure Terminal
Vlan 10
Name ADMIN
Interface Fa0/24
Switchport Mode Access
Switchport access VLAN 10

## Slide 10: Testing & Results
Successful ping within same VLAN
Failed ping across different VLANs

## Slide 11: Challenges & Lessons
Understanding VLAN concepts for the first time.
Assigning correct ports to VLANs.
Troubleshooting failed connectivity tests.
Learning Cisco commands.
The reception laptop not able to connect with the reception Wi-Fi

## Slide 12: Conclusion
VLANs improve security, organization, and network management.

## Slide 13: Future Improvements
Configuring the wireless router
Inter-VLAN routing